LCOV

Following is a quick description of the tracefile format as used by genhtml, geninfo and lcov.

A tracefile is made up of several human-readable lines of text, divided into sections. If available, a tracefile begins with the testname which is stored in the following format:

  TN:<test name>

For each source file referenced in the .da file, there is a section containing filename and coverage data:

  SF:<absolute path to the source file>

Following is a list of line numbers for each function name found in the source file:

  FN:<line number of function start>,<function name>

Next, there is a list of execution counts for each instrumented function:

  FNDA:<execution count>,<function name>

This list is followed by two lines containing the number of functions found and hit:

  FNF:<number of functions found>
  FNH:<number of function hit>

Branch coverage information is stored which one line per branch:

  BRDA:<line number>,<block number>,<branch number>,<taken>

Block number and branch number are gcc internal IDs for the branch. Taken is either '-' if the basic block containing the branch was never executed or a number indicating how often that branch was taken.

Branch coverage summaries are stored in two lines:

  BRF:<number of branches found>
  BRH:<number of branches hit>

Then there is a list of execution counts for each instrumented line
(i.e. a line which resulted in executable code):

  DA:<line number>,<execution count>[,<checksum>]

Note that there may be an optional checksum present for each instrumented line. The current geninfo implementation uses an MD5 hash as checksumming algorithm.

At the end of a section, there is a summary about how many lines were found and how many were actually instrumented:

  LH:<number of lines with a non-zero execution count>
  LF:<number of instrumented lines>

Each sections ends with:

  end_of_record

TN:
SF:/Soft/mag/ut0tyb/prog/lcov/test1.cpp
FN:5,_Z5valuei
FN:13,_Z6value2i
FN:22,_Z6value3i
FN:31,_Z6value4i
FN:41,main
FN:58,_Z41__static_initialization_and_destruction_0ii
FN:59,_GLOBAL__I__Z5valuei
FNDA:6,_Z5valuei
FNDA:7,_Z6value2i
FNDA:3,_Z6value3i
FNDA:0,_Z6value4i
FNDA:1,main
FNDA:1,_Z41__static_initialization_and_destruction_0ii
FNDA:1,_GLOBAL__I__Z5valuei
FNF:7
FNH:6
BRDA:7,0,0,2
BRDA:7,0,1,4
BRDA:8,0,0,2
BRDA:8,0,1,2
BRDA:9,0,0,1
BRDA:9,0,1,1
BRDA:16,0,0,2
BRDA:16,0,1,5
BRDA:17,0,0,3
BRDA:17,0,1,4
BRDA:18,0,0,1
BRDA:18,0,1,6
BRDA:25,0,0,2
BRDA:25,0,1,1
BRDA:26,0,0,1
BRDA:26,0,1,2
BRDA:27,0,0,0
BRDA:27,0,1,3
BRDA:34,0,0,-
BRDA:34,0,1,-
BRDA:35,0,0,-
BRDA:35,0,1,-
BRDA:36,0,0,-
BRDA:36,0,1,-
BRDA:58,0,0,1
BRDA:58,0,1,0
BRDA:58,1,2,1
BRDA:58,1,3,0
BRF:28
BRH:19
DA:5,6
DA:7,6
DA:8,4
DA:9,2
DA:10,6
DA:13,7
DA:15,7
DA:16,7
DA:17,7
DA:18,7
DA:19,7
DA:22,3
DA:24,3
DA:25,3
DA:26,3
DA:27,3
DA:28,3
DA:31,0
DA:33,0
DA:34,0
DA:35,0
DA:36,0
DA:37,0
DA:41,1
DA:43,1
DA:44,1
DA:45,1
DA:46,1
DA:47,1
DA:49,1
DA:50,1
DA:51,1
DA:52,1
DA:53,1
DA:55,1
DA:56,1
DA:57,1
DA:58,2
DA:59,1
LF:39
LH:33
end_of_record